## Slide 1: Convolution Neural Network (CNN) for Digital Radio Frequency Memory (DRFM)
EG Friedel
Johns Hopkins University
May 2023
Thesis presentation in conformity with the requirements for the degree of Master of Science
Notes: Introduce yourself. We have come a long way since the acoustic radar and the radar technology continues to evolve… Couple that with Machine learning which is poised to transform every industry. ML signals the arrival of the next industrial revolution. Theme: It will disrupt the traditional way of doing things. Can we used ML for radars? What things could we envision? What are some difficult problems for radars? The question we propose today is …. Does ML approach work for ECM identification and classification? I’ll admit I’m a radar guy and still learning about AI…excited about the idea and the initial results. This presentation hopes to break down a complex problem into understandable concepts.

## Slide 2: Heilmeier Catechism
What are you trying to do?
How is it done today, and what are the limits of current practice?
What is new in your approach and why do you think it will be successful?
Who cares? If you are successful, what difference will it make?
What are the risks?
How much will it cost?
How long will it take?
What are the mid-term and final “exams” to check for success?
Notes: A set of questions credited to Heilmeier that anyone proposing a research project or product development effort should be able to answer.
Relative error is accuracy. Include the units. What is the standard. Define the axis and be prepared to explain.
We don’t usually use neural networks to solve this type of problem. Use the neural as a solver

## Slide 3: What are you Trying to Do?
Evolve the concept of conventional radar digital signal processing techniques
This presentation focuses on a Machine Learning Approach to identify and classify misleading electronic signals in the radar main-lobe.
Success is defined by the identification of an ECM, in this case a Digital Radio Frequency Memory (DRFM) interferer and its different types via the CNN model.
The new CNN model is proposed to be part of the radar’s signal processing chain.
Notes: I want to evolve the idea of the conventional radar in the area of signal processing by using complex algorithms and artificial neural networks to train machines/computers so that they can learn from experience, classify and recognize data/images just like a human brain does.

## Slide 4: How is it Done Today and Limitations
General Solution: Identify Target Interference as Abnormal and Report to Detection Processing
Passive ECM
DRFM
Noise Interference
Deceptive Interference
Spot Noise
Barrage Noise
Random False Targets
Range Bin Masking
Doppler Bin Masking
Range-Doppler Combined
ECM
Active ECM
Communication ECM
Weapon System ECM
Chaff
Decoys
Signature Reduction
Decoys
Expendable Decoys
Towed Decoys
Flares
Electronic Countermeasures (ECM)
T/R
Transmitter
Receiver
Signal Processor
Tracker
Typical Radar
Task Scheduler
Detection Processing
Mission Profile
Receiver Signal Processing
Radar
Control
Processing
Breaks in Receiver Signal Processing
(False Targets are passed through)
DRFM Interferer
DRFM Interferer figure from G. W. Stimson, Introduction to Airborne Radar, 2nd Ed
False Targets from DRFM Interferer
Promotes sub-optional signal processing operation
Degrades detection performance
Hides the real targets, deceiving the Tracker

## Slide 5: Receiver Signal Processing Chain
Signal Processor
Detection Processing
Receiver Signal Processing
FFT
Replica Multiply
IFFT
Matched Filter
Range Doppler Processing
Detections Processing
Output
Output
Baseband IQ Data
Apply CNN at the output of
Range Doppler Processing
Investigate ID of False Targets in the Time Domain for CNN
Detections Processing of Real/False Targets
Identify and Classify
Range Cell Detection
Breaks in Receiver Signal Processing
(False Targets are passed through)
Notes: Apply CNN … here is the disruptive part effecting the normal operation that I believe will have a big impact on how radars of the future handle image classification. Bayesian is the typical approach here (which we will not detail here) but it relies on a preliminary assumption that a probability distribution can definitely be assigned to any parameter of a statistical problem, hence the idea of an adaptative approach that can learn seems more appealing.

## Slide 6: Machine Learning
Input
Hidden
Output
ECM
Prediction of False Targets
Activation Function
Convolution
Notes: Input: The images from the range-doppler map. A human would just see the pictures and without really thinking is drawn to the highlighted or interesting features of a picture. The computer see this as simply individual pixels or as a set of matrices with numbers. The input in is the pixels that are just passed “as is” with no computation to the hidden layers. Computers work well with numbers and given clever mathematics can pick out patterns and model our ideas through simulation. Quote George Box… All models are wrong, but some are useful.
Hidden: Image a brain with a dense connection of neurons take in a set of weighted inputs and produce an output through an activation function. It is a typical part of nearly any neural network in which engineers simulate the types of activity that go on in the human brain. Here we use convolutional neural networks that focus on image processing. There can be many hidden layers that represent the pixels. This is the key to solving complex non-linear problems. Remove the hidden layer and you would have a model similar to linear regression. Here is where the learning takes place and convolution is the key! Convolutional Neural Nets (CNNs) process an input with layers of kernels, optimizing their weights (plans) to reach a goal. Imagine tweaking the COVID medicine to optimize or prevent the spread and lethality of the disease. This provides an abstraction to the neural network
Output: This is the prediction, identification (false) and classification of the input data. Each time we pass through the model and train we hope to learn more and thus strengthen our model to make the correct predictions.

## Slide 7: Samples of Training Data
Range Bin masking
Doppler Bin masking
Combined masking
Random masking
DRFM Categories
Range Bin masking
Random masking
Random masking
Random masking
Doppler Bin masking
Combined masking
Range-Doppler Images

## Slide 8: Results
Model trained in just a few minutes with 4000 images
Good results with a neural network that has NOT been tuned

## Slide 9: Success what difference will it make?
Opens the door to Machine Learning techniques that demonstrate better radar operational performance and computational saving over existing techniques for radar signal processing
Identification and classification is the first step for applying machine learning techniques to radar signal processing
CNN has been demonstrated in current research as a good and accurate approach for radar signal classification
Adapting to recognition of DRFM targets by moving from a knowledge-based system (domain knowledge) to a learned knowledge approach
An accurate CNN model is a highly attractive solution for non-liner expression capability

## Slide 10: Risks
CNN model accuracy is highly dependent on the training data. Bad training data will produce bad results, also overfitting can occur
Large datasets are typically required to train the neural network. Some architectures can be very complex with many layers
CNN works only on images input and does not work well with timeseries data

## Slide 11: Other Areas of Exploration (Future Work)
Image Segmentation to separate potentially the real and false targets
Design a machine learning approach for time series data
Expand the training data to many other types of interferes and interference
Explore other Neural networks and predictive behavior techniques

## Slide 12: Background

## Slide 13: AI
Artificial Intelligence
Machine Learning
Neural Networks
Deep Learning
CNN
Any technique that allows a machine or computer to solve tasks in a human like way.
Gives a computer the ability to learn without explicitly being programmed.
Machine learning models based on the way a human brain learns.
A machine learning approach that uses several layers of neural networks to build data representations.
A deep learning approach using convolutional neural networks.

## Slide 14: Activation Function

## Slide 15
Ideal situation
  Ideally radar signal processing should be able to accurately and efficiently detect false or misleading electronic signals. Separating the real signals from the false.
Reality
  Typical radar signal processing is ineffective against false targets produced by electronic jammers. Complex ECM jammers are particularly difficult to detect.
Consequences
  Failure to identify false and targets results in the following issues
      Promotes sub-optional signal processing operation
      Degrades detection performance
      Hides the real targets, deceiving the Tracker
Proposal
  Opportunities exist for improved electronic jammer mitigation through machine learning to identify false targets and interference to improve overall radar performance operation.
Problem Statement

## Slide 16: Thesis Objectives
Design and build a MATLAB radar testbed using applied mathematical principles
  Output complex IQ for detection and signal processing
  Demonstrate the problem with typical signal processing
Identify radar signal jamming and classify by using and developing unique mathematical algorithms that exploit machine learning techniques
  TBD % accuracy for each jammer class type
  Performance classification < TBD (sec)
Utilize latest GPU computer hardware
  Apply established software frameworks and programming languages
  Execute a series of iterative experiments that explore fast and slow time CNN inputs over the established hyperparameters
Develop metrics and evaluation criteria to support the claim that machine learning can be an effective technique for radar DRFM jammer classification
  Outperforms classical signal processing techniques against an evolving DRFM technology.
  Reduces radar signal processing loads and computation times

## Slide 17: What are your main contributions?
A new CNN model or solution for DRFM jammers
A novel method using stochastic techniques for detection processing for the separation of false and real targets
What trades or experiments did you perform?
Any Limitations?
Future Work …

## Slide 18: Why use Neural Networks to solve this problem?
Helps to support the idea of jamming suppression prior to the application of the matched filter for target detection processing
Plan to show that CNN feature extraction of DRFM jamming signals can be more efficient and superior then conventional radar signal processing techniques
An accurate CNN model is a highly attractive solution for a non-linear expression capability. This is what we hope to achieve!
We frame this as a target detection problem that can be addressed with image classification. CNNs have made great progress in this area along with computer vision. So, machine learning in general seems to be a good fit for this problem.

## Slide 19: Where does the standard approach break?
Due to the strong correlation of the false target to the transmitted signal, the matched filter gets applied and thus processed as a real target.
  The matched filter is the basic technique used for most radar signal processing designs.
  Main-lobe jamming is difficult to detect because of the matched filter processing used by the radar.
Loss of target information and model mismatch are problematic when a radar is being jammed. The standard parametric approach is ill-fitted because it relies apriori mission information.
We should investigate more closely other detection methods to support the matched filter. The problem is the false targets are in the main-lobe of the beam.
  Waveform or frequency agility would change the replica of the matched filter, but this would not help for DRFM false targets which matches the transmitted pulse of the radar
  Adaptive waveforms are used to put the false targets in null of the beam however in this case, you would lose your real target and thus should not be used
  CFAR will help with false alarms and some false targets by adjusting the detection threshold level but would have little to no effect on main-lobe detections near or exceeding the real target SNR.

## Slide 20: Where does the standard approach break?
Due to the strong correlation of the false target to the transmitted signal, the matched filter gets applied and thus processed as a real target.
  The matched filter is the basic technique used for most radar signal processing designs.
  Main-lobe jamming is difficult to detect because of the matched filter processing used by the radar.
Loss of target information and model mismatch are problematic when a radar is being jammed. The standard parametric approach is ill-fitted because it relies apriori mission information.
We should investigate more closely other detection methods to support the matched filter. The problem is the false targets are in the main-lobe of the beam.
  Waveform or frequency agility would change the replica of the matched filter, but this would not help for DRFM false targets which matches the transmitted pulse of the radar
  Adaptive waveforms are used to put the false targets in null of the beam however in this case, you would lose your real target and thus should not be used
  CFAR will help with false alarms and some false targets by adjusting the detection threshold level but would have little to no effect on main-lobe detections near or exceeding the real target SNR.

## Slide 21: Challenges
Radar Model with Applied Mathematics
      Careful not to reveal any proprietary information
Training Data
      Reducing the amount of training time
        Reducing the size of the training data and still maintain desired accuracy and performance. Idea for dominant features, akin to reduced scattering center RCS modeling approach.
        Adjust the number of layers max-pooling layers.
        Including dropout, convolution, batch normalization layer for ease of use
        Use GPUs to accelerate the calculation process.
Image Classification
      Selecting the image features that provide the best results and identify each class with the desired accuracy
      Time-series classification
Architecture
      Designing mathematical algorithms that demonstrate performance enhancements over existing techniques for a CNN.
          Look at gradient descent strategies

## Slide 22
Beamformer Adaption for Noise Jammer
Prior work done to help address noise jammers, where the angle of interference is known

## Slide 23: Deceptive Jammer Top-level Architecture
ES
(Digital Rx)
Memory
WF Generator
Technique Generator
DAC
~
Rx
Tx
Rx
Tx
Electronic Support Measures
Electronic Attack
Typically uses digital radio frequency memory (DRFM)
Captures the victim waveform and applies delays and/or Doppler shifts to the waveform before retransmitting it (e.g. range gate stealer, velocity gate stealer)
Tx and Rx antennas can be shared or separate – periodic monitoring of the environment is required
Exploits coherence with the victim radar to reduce jammer power requirements

## Slide 24: Cover Pulse
Cover pulse uses a transponder that produces range-gated noise triggered off of the pulses received from the radar
Improves energy efficiency of the jamming by enabling it to reduce the average power needed to ‘cover’ the target
Cover pulse captures the CFAR noise floor estimate resulting in a missed detection
Typical J/S of 10-40 dB
Transponder
Block diagram from G. W. Stimson, Introduction to Airborne Radar, Scitech, 1998
target detection missed
To test a cell in the center of here
Estimate local noise over the cells outside here but inside here
Normalize cell by noise floor estimate; compare to threshold

## Slide 25: Bin Masking
Range bin masking denies victim radar the target range – often used in low and medium PRF radars
Doppler bin masking denies radar target Doppler
  Typically used against medium and high PRF systems
  Can produce using a variety of slow-time phase modulations
Repeater for producing range bin masking
Straight-through Repeater for producing Doppler bin masking
Range Bin Masking
Doppler Bin Masking
Block diagrams from G. W. Stimson, Introduction to Airborne Radar, 2nd Ed Scitech, 1998

## Slide 26: Range and Doppler Bin Masking
Can mask multiple range and Doppler bins at once
Range and Doppler bin masking can capture typical CA CFAR and prevent detection of the skin
Can be produced using DRFM-based repeater
Typical J/S of 10-20 dB
with jamming
detection missed
without jamming
To test a cell in the center of here
Estimate local noise over the cells outside here but inside here
Normalize cell by noise floor estimate; compare to threshold

## Slide 27: False Target Range-Doppler Maps
Various false target configurations are possible depending on the jammer sophistication

## Slide 28: False Target CA CFAR Maps
False target returns can consume radar resources as additional confirm dwells and tracks must be pursued
Additionally, a high-power stand-off jammer can inject false targets into the sidelobes, providing a form of angle deception (though this can be countered)

## Slide 29: Gate Pull-off Illustration
FT initially on top of target, significantly stronger than skin return
As FT pulls off the target, it takes the track window with it; can suppress true target in CFAR output
FT pulls track window off target – even though target is now detectable, radar is only looking in the window

## Slide 30: Sidelobe Blanking
Compare output of mainbeam and guard channel
If the difference exceeds a design threshold, a mainbeam detection is declared
If the difference does not exceed the threshold, a sidelobe detection is declared – potential false target injected into sidelobes
mainbeam ouput guard channel output
ðmainbeam detection
nominal mainbeam-to-sidelobe ratio
mainbeam ouput guard channel output
ð sidelobe detection
mainbeam output
guard channel output
mainbeam output
guard channel output
Figure modified from G. W. Stimson, Introduction to Airborne Radar, Scitech, 1998

## Slide 31: Jittered PRI
Change PRI from one pulse to the next
Prevents deception jamming from generating consistent false targets from pulse-to-pulse
True targets will resolve to consistent ranges
Leading false targets get rejected
Amount of jitter will be limited if using pulse-Doppler operation
Clutter cancellation is similarly complicated – modulation of clutter results in greater Doppler spread
On the order of 5% jitter may still allow for pulse-Doppler operation – need sufficient range resolution to detect resulting range inconstancies
solid – true target; dashed – false target

## Slide 32: Mask Detection
Recall (continuous) noise jamming detector
  Perform on envelop-detected cells
  Choose a test region that covers a wide area to distinguish noise jamming from localized interference
  If cells out of cells tested exceed a threshold then noise jamming is declared
‘Local’ masking (cover pulse, bin masking) and false target jamming will fail this test and not be detected
Solution (for masking)
  Perform the dual-threshold test over localized regions
  Use ordered statistic detector
Notional Search Mode Test Region
(high-altitude, no clutter case)
Doppler
range

## Slide 33: Other Pull-off Detection Techniques
Harmonics detection
  VGPO and R-VGPO use modulation to produce velocity walk-off
  If the modulation is not perfectly clean, it can, coupled with the large signal required, produce harmonics in the return
  Provides a jamming indication
RCS Measurements
  RGPO or VGPO uses a large signal return to capture the tracking window
  This sudden increase in signal power can be an indication of jamming (need to guard against false alarms)
before jamming
after jamming starts

## Slide 34: False Target Detection
Doppler false targets often periodic in frequency and centered about the true target
Doppler false targets are all at the same range, can track target in range / discriminate in tracker
Numerous targets that all have the same angle of arrival (to within the measurement error of the system) are candidate false targets
Exploit tracking over time to detect inconsistencies between the range and Doppler measurements of the false target (also for pull-off techniques)
Track measured RCS
  false target signals will typically have unrealistic statistics over time
  e.g., the measured RCS will exhibit less fluctuation since the jammer wants the radar to see the target with few missed detections due to fluctuations in order to keep the display flooded

## Slide 35: Leading Edge Detection Cover Pulse
CA CFAR
  cell-averaging CFAR
  Use average of cells over a window as the noise floor estimate
TM CFAR
  Trimmed-mean CFAR
  Excise top and bottom cells from window prior to averaging
  gives the median CFAR
CFAR output gives some indication of jamming
Since jammer response cannot precede target response, CFAR noise floor estimate indicates the jammer range

## Slide 36: Bin Mask Leading Edge Detection
If the leading edge of the mask can be detected, the range to the jammer can be measured
Key is to determine the appropriate technique to identify the leading edge of the mask
Note – techniques that use ‘prediction’ to go up range of the jammer will negate leading edge tracking
Mask raises the CFAR noise estimate, causing a missed detection
Median CFAR provides more of an indication of the mask shape
CFAR mask = 5 Dop x 13 range gates (use every other range gate)
CFAR mask = 25 Dop x 1 range gate (use every other Dop filt)
Leading edge of mask better revealed with median CFAR

## Slide 37: Summary
Deceptive jammers try to confuse radar
  Hide skin return (similar to noise jamming)
  Overwhelming detection processing (false targets)
  Deceive tracker
No single EP technique; use multiple approaches including:
  Make radar waveforms difficult to identify
    Various radar waveforms (HPRF, MPRF, different pulse widths)
    Short time on RF
    Wide bandwidth (jammer needs to find radar)
  Recognize jamming returns as ‘abnormal’
    Report degraded performance
    Reset to target skin return
  Difference between Kalman and Doppler trackers can trigger pull-off detection
  Build in EP from the beginning – hardware and software
  Additional techniques to consider include LPI waveforms and power management
Multiple complimentary sensors – each has its own weaknesses and strengths (see table at right)
EA & EP discussed these modules is not exhaustive – other techniques can be employed
Red bold indicates potential vulnerabilities
Table from G. W. Stimson, Introduction to Airborne Radar, 2nd Ed, Scitech, 1998

## Slide 38: References
G. W. Stimson, Introduction to Airborne Radar, 2nd Edition, SciTech, 1998
G. W. Stimson, Introduction to Airborne Radar, 3rd Edition, IET, 2014
D. K. Barton, Radar System Analysis and Modeling, Artech House
R. N. Lothe, M. B. Szymanski, and R. G. Wiley, Radar Vulnerability to Jamming, Artech House
R. G. Wiley, ELINT, The Interception and Analysis of Radar Signals, Artech House
M. I. Skolnik, Ed., Radar Handbook, McGraw-Hill
A. Partizian, “Electronic protection,” in Principles of Modern Radar, Vol. II: Advanced Techniques, W. L. Melvin and J. A. Scheer, Eds. Edison, NJ: SciTech Publishing, 2013, ch. 12, pp. 529-585
S. L. Johnston, “Radar electronic counter-countermeasures, IEEE Transactions on Aerospace and Electronic Systems, January, 1978
Electronic Warfare, Joint Publication 3-13.1, https://www.hsdl.org/?abstract&did=469779
Joint Electromagnetic Spectrum Operations, Joint Publication 3-85, https://www.jcs.mil/Doctrine/Joint-Doctrine-Pubs/3-0-Operations-Series/
Electronic Warfare and Radar Systems Engineering Handbook, https://apps.dtic.mil/dtic/tr/fulltext/u2/a617071.pdf
Electronic Warfare Fundamentals, http://falcon.blu3wolf.com/Docs/Electronic-Warfare-Fundamentals.pdf
https://www.radartutorial.eu/16.eccm/ja05.en.html